PULSES ON A COIL SPRING

TRANSVERSE PULSES

A. Send a transverse pulse down a stretched large coil spring.  Observe the motion of the

spring’s coils.  Draw a sketch of the pulse traveling down the spring.

Why is this pulse called a transverse pulse?

B. Observe the speed of the pulse while varying the pulse amplitude.  What happens to the

speed of the pulse as the amplitude changes?

C. Observe the speed of the pulse while varying the tension in the spring.  What do you notice

about the pulse speed with respect to changes in tension?

D. Does the stretched spring under different tensions represent the same or different

transmitting media?

E. Maintain a constant tension and send continuous wave trains of varying frequencies down

the spring.  What happens to the wavelength as the frequency increases?

WAVE INTERFERNCE

F. Send two pulses of approximately the same amplitude from opposite ends of the spring

toward each other on the same side of the spring.  What do you observe?

Do the two disturbances “bounce off” each other or pass right through each other?

What do you notice when the pulses “overlap”?

Draw sketches showing the pulses, labeled “A” and “B”, before, during, and after they

meet.

G. Send two pulses of approximately the same amplitude from opposite ends of the spring

toward each other on opposite sides of the spring.  What do you observe?

Do the two disturbances “bounce off” each other or pass right through each other?

What do you notice when the pulses “overlap”?

Draw sketches showing the pulses (labeled “A” and “B”) before, during, and after they

meet.

WAVE REFLECTION

H. Hold the spring firmly down in place at the far end and send a pulse down the spring.

Describe and illustrate your observations of reflection from this “fixed end.”

I. Attach and hold a light string on one end of the spring and send a pulse from the other

end.  Describe and illustrate your observations of reflection from this “free end.”

STANDING WAVES

J. While holding one end of the large spring firmly in place, move the other end of the spring

continuously back and forth to send a continuous wave train down the spring.  Adjust your

frequency until a standing wave with two “loops” is obtained.

Now change your frequency of vibration until more loops are formed.  Since the speed of

the wave remains constant (do you know why?), shaking the spring with a higher frequency

does what to the wavelength?

In order to obtain standing waves with more loops when the speed of the wave is constant,

what must be done to the frequency of vibration?

How could you determine the wavelength of the wave when a standing wave pattern is

observed?

Draw sketches of standing waves having one, two, three, and four loops.  Indicate on your

sketches how the wavelength could be measured.

LONGITUDINAL PULSES

K. Stretch the large spring and send a longitudinal pulse down the spring.  Observe the

motion of the spring coils.  Draw a sketch of the pulse traveling down the spring.

Why is this pulse called a longitudinal pulse?

Note:

Wave properties such as diffraction and refraction unfortunately cannot be observed with coiled springs.

# Text boxes

Coiled springs are excellent materials for analyzing a variety of wave behaviors.  In

this activity, you will examine transverse and longitudinal pulses, fixed- and free-end reflections, constructive and destructive interference, standing waves, and the behavior of waves when they reach new transmitting media.